## Slide 1
Unit - 4: Registers and Counters
REGISTERS:
A clocked sequential circuit consists of a group of flip‐flops and combinational gates. The flip‐flops are essential because, in their absence, the circuit reduces to a purely combinational
circuit.
A register is a group of flip‐flops, each one of which shares a common clock and is capable of storing one bit of information.
An n ‐bit register consists of a group of n flip‐flops capable of storing n bits of binary information.
In addition to the flip‐flops, a register may have combinational gates that perform certain data‐processing tasks.

## Slide 2
FIGURE: Four‐bit register

## Slide 3
Register with Parallel Load
FIGURE: Four‐bit register with parallel load

## Slide 4
SHIFT REGISTERS:
A register capable of shifting the binary information held in each cell to its neighboring cell, in a selected direction, is called a shift register.
The logical configuration of a shift register consists of a chain of flip‐flops in cascade, with the output of one flip‐flop connected to the input of the next flip‐flop.
All flip‐flops receive common clock pulses, which activate the shift of data from one stage to the next.
The simplest possible shift register is one that uses only flip‐flops, as shown in the following Fig. The output of a given flip‐flop is connected to the D input of the flip‐flop at its right. This shift register is unidirectional (left‐to‐right). Each clock pulse shifts the contents of the register one bit position to the right.

## Slide 5
FIGURE: Four‐bit shift register
Serial Transfer

## Slide 6
FIGURE: Serial transfer from register A to register B

## Slide 7
Serial Addition:
FIGURE: Serial adder

## Slide 8
The operation of the serial adder is as follows:
Initially, register A holds the augend, register B holds the addend, and the carry flip‐flop is cleared to 0.
The outputs ( SO ) of A and B provide a pair of significant bits for the full adder at x and y.
Output Q of the flip‐flop provides the input carry at z.
The shift control enables both registers and the carry flip‐flop, so at the next clock pulse, both registers are shifted once to the right, the sum bit from S enters the leftmost flip‐flop of A, and the output carry is transferred into flip‐flop Q.

## Slide 9
Redesign the serial adder with the use of a state table (using JK flip-flop.):

## Slide 10
FIGURE: Second form of serial adder using JK Flip-flop.

## Slide 11
Universal Shift Register:
Some shift registers provide the necessary input and output terminals for parallel transfer. They may also have both shift‐right and shift‐left capabilities.
The most general shift register has the following capabilities:
1. A clear control to clear the register to 0.
2. A clock input to synchronize the operations.
3. A shift‐right control to enable the shift‐right operation and the serial input and output lines associated with the shift right.
4. A shift‐left control to enable the shift‐left operation and the serial input and output lines associated with the shift left.
5. A parallel‐load control to enable a parallel transfer and the n input lines associated with the parallel transfer.
6. n parallel output lines.

## Slide 12
7. A control state that leaves the information in the register unchanged in response to the clock. Other shift registers may have only some of the preceding functions, with at least one shift operation.
A register capable of shifting in one direction only is a unidirectional shift register.
One that can shift in both directions is a bidirectional shift register. If the register has both shifts and parallel‐load capabilities, it is referred to as a universal shift register.

## Slide 13
FIGURE: Four‐bit universal shift register

## Slide 14
HDL FOR REGISTERS AND COUNTERS:

## Slide 15
Consider the following alternative case statement for the shift register model:
Without the case item 2’b00, the case statement would not find a match between {s1, s0} and the case items, so register A_par would be left unchanged.

## Slide 16
A structural model of the universal shift register can be described by referring to the logic diagram of Fig. (b).
The diagram shows that the register has four multiplexers and four D flip‐flops.
A mux and flip‐flop together are modeled as a stage of the shift register. The stage is a structural model, too, with an instantiation and interconnection of a module for a mux and another for a D flip‐flop.
For simplicity, the lowest‐level modules of the structure are behavioral models of the multiplexer and flip‐flop. Attention must be paid to the details of connecting the stages correctly.
The top‐level module declares the inputs and outputs and then instantiates four copies of a stage of the register.
The four instantiations specify the interconnections between the four stages and provide the detailed construction of the register as specified in the logic diagram.

## Slide 21
RIPPLE COUNTERS:
Binary Ripple Counter:
A binary ripple counter consists of a series connection of complementing flip‐flops, with the output of each flip‐flop connected to the C input of the next higher order flip‐flop.
The flip‐flop holding the least significant bit receives the incoming count pulses.
A complementing flip‐flop can be obtained from a JK flip‐flop with the J and K inputs tied together or from a T flip‐flop.
A third possibility is to use a D flip‐flop with the complement output connected to the D input.

## Slide 22
FIGURE: Four‐bit binary ripple counter with T Flip-flops.

## Slide 23
FIGURE: Four‐bit binary ripple counter with D Flip-flops.

## Slide 24
BCD Ripple Counter:
A ripple counter is an asynchronous sequential circuit. Signals that affect the flip‐flop transition depend on the way they change from 1 to 0.
FIGURE: State diagram of a decimal BCD counter
Remember that when the C input goes from 1 to 0, the flip‐flop is set if J = 1, is cleared if K = 1, is complemented if J = K = 1, and is left unchanged if J = K = 0.

## Slide 25
Q1 changes state after each clock pulse.
Q2 complements every time Q1 goes from 1 to 0, as long as Q8 = 0.
When Q8 becomes 1, Q2 remains at 0.
Q4 complements every time Q2 goes from 1 to 0.
Q8 remains at 0 as long as Q2 or Q4 is 0. When both Q2 and Q4 become 1, Q8 complements when Q1 goes from 1 to 0.
Q8 is cleared on the next transition of Q1.
The BCD counter of above Fig. is a decade counter, since it counts from 0 to 9. To count in decimal from 0 to 99, we need a two‐decade counter. To count from 0 to 999, we need a three‐decade counter.
A three‐decade counter is shown in the following Fig. The inputs to the second and third decades come from Q8 of the previous decade. When Q8 in one decade goes from 1 to 0, it triggers the count for the next higher order decade while its own decade goes from 9 to 0.

## Slide 26
FIGURE: BCD ripple counter

## Slide 27
FIGURE: Block diagram of a three‐decade decimal BCD counter