## Slide 1: Signals and Systems UE18EC202

## Slide 2: Motivation
Fundamental subject

## Slide 3: Why study Signals and Systems?
Engineers build systems that process/manipulate signals.
We need a formal mathematical framework for the study of such systems.
Such a framework is necessary in order to ensure that a system will meet the required specifications (e.g., performance and safety).
If a system fails to meet the required specifications or fails to work altogether, negative consequences usually ensue.
When a system fails to operate as expected, the consequences can sometimes be catastrophic.

## Slide 4: OUTCOMES
  Classify systems based on their properties: in particular, exploit the implications of linearity, time-invariance, causality, memory, and bounded-input, bounded-out (BIBO) stability.
  Determine Fourier transforms for continuous-time and discrete-time signals (or impulse-response functions), interpret and plot Fourier transform magnitude and phase functions..
  Use the relationships among the various representations of LTI systems—linear constant-coefficient difference or differential equation, frequency response, transfer function, and impulse response—and infer one representation from another (e.g., determine the impulse response from the difference equation, etc.).

## Slide 5
  Determine the conditions for a time-domain function to have a Fourier transform, and know how to relate the Fourier transform to its Z transform.
  Analyze and design signals and system using transformation technique.
  Use the unilateral Z transform to decompose the response of an LTI system into a zero-state component and a zero-input component, and solve linear, constant-coefficient difference equations, with possibly non-zero initial conditions.
OUTCOMES

## Slide 6: Syllabus
Unit 1 : 10 hrs
Signals and systems :
  Classification of signals
  Continuous-time and discrete-time signals
  Transformations of the independent variable
  Exponential and sinusoidal signals
  The unit impulse and unit step functions
  Continuous-time and discrete-time systems
  Basic system properties.

## Slide 7: Syllabus
Unit 2 : 10 hrs
Linear time-invariant systems:
  Discrete-time LTI systems: The convolution sum
  Continuous-time LTI systems: The convolution integral
  Properties of LTI systems
  Causal LTI systems described by differential / difference equations (Natural, Forced, and Complete Response)

## Slide 8: Syllabus
Unit 3 : 10 hrs
Fourier series representation of periodic signals :
  Response of LTI systems to complex exponentials
  Trigonometric Fourier Series
  Fourier series representation of continuous-time periodic signals
  Convergence of the Fourier series
  Properties of continuous-time Fourier series
  Introduction to Fourier series representation of discrete-time periodic signals.

## Slide 9: Syllabus
Unit 4: 12 hrs
The continuous-time Fourier transform:
  Representation of aperiodic signals: the continuous-time Fourier transform
  The Fourier transform for periodic signals,
  Properties of continuous-time Fourier transform, Fourier transform pairs.
The discrete-time Fourier transform:
  Representation of aperiodic signals: the discrete-time Fourier transform
  The Fourier transform for discrete periodic signals
  Properties of discrete-time Fourier transform, Fourier transform pairs
  Duality. Frequency Response of LTI Systems Magnitude and Phase response.

## Slide 10: Syllabus
Unit 5: 10 hrs
The Z-transform:
  The Z-transform
  The region of convergence for the Z-transform
  The inverse Z-transform
  Properties of the Z-transform
  Z-transform pairs
  Analysis and characterization of LTI systems using Z-transforms.
  The unilateral Z-transform and solution of difference equations.

## Slide 11: Textbook

## Slide 13: What is a Signal?
Signal (dependent variable) is any real world quantity varying with time, space or frequency (independent variable)
Signals are variables that carry information
Examples of signal include:
  Electrical signals
    Voltages and currents in a circuit
  Mechanical signals
    Velocity of a car over time
  Audio and Video signals
  Intensity level of a pixel (camera, video) over time

## Slide 17
AUDIO SIGNAL
SPEECH SIGNAL

## Slide 22: Continuous-Time Signal
Most signals in the real world are continuous time, as the scale is infinitesimally fine.
  Eg voltage & current, pressure, temperature, velocity, etc.
Denoted by x(t), where the time interval may be bounded (finite) or infinite
x(t)
t

## Slide 23: Discrete time signal
Some real world and many digital signals are discrete time, as they are sampled
  E.g. pixels, daily stock price (anything that a digital computer processes)
Denoted by x[n], where n is an integer value that varies discretely
x[n]
n
Many human-made Signals are DT

## Slide 24: System
A collection of items that together performs a function
Modifies / transforms an input to give an output
Represented by
System
T{ }
x(t)
y(t) = T{x(t)}
T = input2
x(t)
y(t) = T{x(t)} = x2(t)
ex. A squaring system

## Slide 25: Real-World Examples of Systems
Circuits
Car
  Inputs  Steering wheel, force on accelerometer and brakes
  Outputs  Position of car, velocity
Chemical processes
Electromechanical systems (motors)
Economics, stock market
Biological processes (heart)

## Slide 26: Communication system

## Slide 28: Biomedical system

## Slide 30: Auditory system

## Slide 31: Two types of systems
Continuous-time systems
  Operate on continuous-time signals
  Represented mathematically using differential equations
  System parameters are defined on a continuum of time
Discrete-time systems
  Operate on discrete-time signals
  Represented mathematically by difference equations
  System parameters are defined only at discrete points in time

## Slide 32: Classification of Signals
Number of independent variables (i.e., dimensionality):
  A signal with one independent variable is said to be
    one dimensional (e.g.,audio).
  A signal with more than one independent variable is said to be
    multi-dimensional (e.g., image).
Continuous or discrete independent variables:
  A signal with continuous independent variables is said to be continuous time (CT) (e.g., voltage waveform).
  A signal with discrete independent variables is said to be discrete time (DT) (e.g., stock market index).
Continuous or discrete dependent variable:
  A signal with a continuous dependent variable is said to be continuous valued (e.g., voltage waveform).
  A signal with a discrete dependent variable is said to be discrete valued (e.g., digital image).
A continuous-valued CT signal is said to be ANALOG (e.g., voltage waveform).
A discrete-valued DT signal is said to be DIGITAL (e.g., digital audio).

## Slide 33: Size of a Signal !!!
The size of any entity is a number that indicates the largeness or the strength of that entity.
Generally, signal amplitude varies with time.
Is it possible to provide a measure of the varying amplitude by one number ?
That measure must consider not only the signal amplitude, but also duration.
For example, Let V be a measure of the size of a human being.
  Width (grith) and
  Height

## Slide 34
With the previous analogy, consider the area under a signal as a possible measure of its size. It takes account of
  Amplitude

## Slide 35: Signal Energy
With the previous analogy, consider the area under a signal as a possible measure of its size. It takes account of
  Amplitude
  Time duration
  i.e
But, with the above measure there is a chance that positive and negative cycle can cancel each other and indicating a signal of small size !!!!
This difficulty is surmounted as
This is called as Signal Energy

## Slide 36: Signal Energy
With the previous analogy, consider the area under a signal as a possible measure of its size. It takes account of
  Amplitude
  Time duration
  i.e
But, with the above measure there is a chance that positive and negative cycle can cancel each other and indicating a signal of small size !!!!
This difficulty is surmounted as
or
for complex valued signal
This is called as Signal Energy
Notes: It is indicative of the energy that can be extracted from the signal

## Slide 37: Signal Power
The signal energy must be finite for it to be meaningful measure of the signal size.
The condition for the energy to be finite is that the signal amplitude should become zero asymptotically.
  Otherwise, the integral will not converge.
Therefore, a meaningful measure of the signal size in such case would be the time average of the energy (if it exists).
  i.e
This measure is called Signal Power.
when is complex valued signal

## Slide 38: Discrete time signals
Signal Energy
Signal Power

## Slide 39: Transformations of the Independent Variable

## Slide 40: Time Shift (Translation)
Time shifting (also called translation) maps the input signal x to the output signal y as given by
where b is a real number for CT Signal and b is a Integer for DT Signals.
Such a transformation shifts the signal (to the left or right) along the time axis.
If b > 0, y is shifted to the right by |b|, relative to x (i.e., delayed in time).
If b < 0, y is shifted to the left by |b|, relative to x (i.e., advanced in time).

## Slide 43: Time Reversal (Reflection)
Time reversal (also known as reflection) maps the input signal x to the output signal y as given by
Geometrically, the output signal y is a reflection of the input signal x about the (vertical) line t = 0.

## Slide 44: Time Scaling
Time compression/expansion (also called dilation) maps the input signal x to the output signal y as given by
where a is a strictly positive real number for CT and DT Signals.
Such a transformation is associated with a compression/expansion along the time axis.
If a > 1, y is compressed along the horizontal axis by a factor of a, relative to x.
If a < 1, y is expanded (i.e., stretched) along the horizontal axis by a factor of , relative to x.

## Slide 46
K an integer > 1

## Slide 47: Combined Time Scaling and Time Shifting
Consider a transformation that maps the input signal x to the output signal y as given by
where a and b are real numbers and a ≠ 0.
The above transformation can be shown to be the combination of a time-scaling operation and time-shifting operation.
Since time scaling and time shifting do not commute, we must be particularly careful about the order in which these transformations are applied.
The above transformation has two distinct but equivalent interpretations:
    1. first, time shifting x by b, and then time scaling the result by a
    2. first, time scaling x by a, and then time shifting the result by b/a.
Note that the time shift is not by the same amount in both cases.

## Slide 49: Signal Classification
Analog and Digital Signals
Deterministic and Random Signals
Even and Odd Signals
Periodic and Aperiodic Signals
Energy and Power Signals
Multi-dimensional and Multi Channel Signals

## Slide 53: Deterministic Signals
Deterministic signal is a signal exhibiting no uncertainty of value at any given instant of time. Its instantaneous value can be accurately predicted by mathematical equation.
  Ex:

## Slide 58: Even and Odd function: Sum and Product
Sums involving even and odd functions have the following properties:
  The sum of two even functions is even.
  The sum of two odd functions is odd.
  The sum of an even function and odd function is neither even nor odd, provided that neither of the functions is identically zero.
That is, the sum of functions with the same type of symmetry also has the same type of symmetry.
Products involving even and odd functions have the following properties:
  The product of two even functions is even.
  The product of two odd functions is even.
  The product of an even function and an odd function is odd.
That is, the product of functions with the same type of symmetry is even, while the product of functions with opposite types of symmetry is odd.

## Slide 61
Sum of periodic functions. Let x1 and x2 be periodic functions with fundamental periods and , respectively. Then, the sum y = x1 +x2 is a periodic function if and only if the ratio is a rational number (i.e., the quotient of two integers). Suppose that = q/r where q and r are integers and coprime (i.e., have no common factors), then the fundamental period of y is r (or equivalently, q, since r = q). (Note that r is simply the least common multiple of and .)
Although the above theorem only directly addresses the case of the sum of two functions, the case of N functions (where N > 2) can be handled by applying the theorem repeatedly N −1 times.

## Slide 66
The energy of this signal is the shaded region

## Slide 67
The energy of this signal is the shaded region

## Slide 69
    Deterministic Aperiodic signals are Energy Signals

## Slide 73
Causal and Anticausal Signals
Causal signals : zero for all negative time
Anticausal signals : zero for all positive time
Noncausal : non-zero values in both positive and negative time
causal signal
anticausal signal
noncausal signal

## Slide 74
Elementary signals

## Slide 75
Elementary signals
Impulse
Step
Ramp
Sinusoidal
Real exponential
Complex exponential
Signum
Sinc
Triangle
Rectangle
Parabolic

## Slide 76
The Discrete-Time Unit Impulse Function
(Dirac or Delta function)
-4 -3 -2 -1 0 1 2 3 4

## Slide 77
The Discrete-Time Unit Step Function
-4 -3 -2 -1 1 2 3 4

## Slide 78: Relation between Step function and Delta function
The discrete time impulse is the first difference of the discrete time step
The discrete time unit step is the running sum of the unit impulse
It can be seen that for , the running sum is 1.
If we change the variable of summation from we have

## Slide 80
There is a close relation between , and
r

## Slide 82: Unit Step
The unit-step function (also known as the Heaviside function), denoted , is defined as
Due to the manner in which is used in practice, the actual value of is unimportant. Sometimes values of and are also used for .
A plot of this function is shown below.

## Slide 89: Exponential and Sinusoidal Signals

## Slide 90: Real Sinusoids
A (CT) real sinusoid is a function of the form
),
where and are real constants.
Such a function is periodic with fundamental period and fundamental frequency .
A real sinusoid has a plot resembling that shown below.

## Slide 91: Complex Exponentials
A (CT) complex exponential is a function of the form
,
where and are complex constants.
A complex exponential can exhibit one of a number of distinct modes of behavior, depending on the values of its parameters and.
For example, as special cases, complex exponentials include real exponentials and complex sinusoids.

## Slide 92: Real Exponential
A (CT) real exponential is a function of the form
,
where and are real constants.
A real exponential can exhibit one of three distinct modes of behavior, depending on the value of .
If > 0, x(t) increases exponentially as t increases (i.e., a growing exponential).
If < 0, x(t) decreases exponentially as t increases (i.e., a decaying exponential).
If = 0, x(t) simply equals the constant A
Notes: e as “a constant approximately 2.71828…” is like calling pi “an irrational number, approximately equal to 3.1415…”

## Slide 96: Complex Sinusoid
A complex sinusoid is a special case of a complex exponential
where A is complex and is purely imaginary (i.e., Re{} = 0).
That is, a (CT) complex sinusoid is a function of the form
,
where A is complex and 𝜔 is real.
By expressing A in polar form as (where is real) and using Euler’s relation, we can rewrite x(t) as
Thus, and are the same except for a time shift.
Also, x is periodic with fundamental period and fundamental frequency .

## Slide 98: General Complex Exponential
In the most general case of a complex exponential , and are both complex.
Letting and (where , and are real), and using Euler’s relation, we can rewrite as
Thus, and are each the product of a real exponential and real sinusoid.
One of three distinct modes of behavior is exhibited by , depending on the value of.
  If , and are real sinusoids.
  If , and are each the product of a real sinusoid and a growing real exponential.
  If , and are each the product of a real sinusoid and a decaying real exponential.

## Slide 100: Relationship Between Complex Exponentials and Real Sinusoids
From Euler’s relation, a complex sinusoid can be expressed as the sum of two real sinusoids as
Moreover, a real sinusoid can be expressed as the sum of two complex sinusoids using the identities

## Slide 101: Discrete-Time Complex Exponentials and Sinusoidal Signals

## Slide 102: DT Real Sinusoids
A (DT) real sinusoid is a sequence of the form
where and 𝛉 are real constants.
A real sinusoid is periodic if and only if is a rational number, in which case the fundamental period is the smallest integer of the form where k is a positive integer.
For all integer k, is the same sequence.
An example of a periodic real sinusoid with fundamental period 12 is shown plotted below.

## Slide 105
Notes: = = 4
"𝝮" _0 𝑛_0 =𝜋/2 𝜋/8 𝑛_0 = 𝜋/2 〖 𝑛〗_0 = 4

## Slide 111: Complex Exponentials
A (DT) complex exponential is a sequence of the form
,
where and are complex constants.
A complex exponential can exhibit one of a number of distinct modes of behavior, depending on the values of the parameters c and a.
For example, as special cases, complex exponentials include real exponentials and complex sinusoids.

## Slide 112: Real Exponentials
A (DT) real exponential is a special case of a complex exponential
where c and a are restricted to be real numbers.
A real exponential can exhibit one of several distinct modes of behavior, depending on the magnitude and sign of a.
If |a| > 1, the magnitude of x[n] increases exponentially as n increases (i.e., a growing exponential).
If |a| < 1, the magnitude of x[n] decreases exponentially as n increases (i.e., a decaying exponential).
If |a| = 1, the magnitude of x[n] is a constant, independent of n.
If a > 0, x[n] has the same sign for all n.
If a < 0, x[n] alternates in sign as n increases/decreases.

## Slide 119: Complex Sinusoids

## Slide 121: General Complex Exponential

## Slide 127
Ramp signal
Unit step

## Slide 128
SYSTEMS AND CLASSIFICATION OF SYSTEMS (BASED ON PROPERTIES)

## Slide 129: Systems

## Slide 130: Continuous Time and Discrete Time Systems

## Slide 131
Notes: Often, a system defined by the operator H and having the input x and
output y is represented in the form of a block diagram as shown below.

## Slide 134: Series (Cascade) and Parallel
Interconnecting Systems

## Slide 135: Feedback Systems

## Slide 138
Classification of Systems (based on Properties)
  Static and Dynamic Systems
  Invertible and Non-invertible systems
  Time-Variant and Time-Invariant systems
  Linear and Non-linear systems
  Causal and Non-causal systems
  Memory and Memoryless Systems
  Stable and Unstable systems

## Slide 139
Static and Dynamic Systems
When the output of the system depends only upon the present input sample, then system is called static system
Hence such Systems do no need memory for its operation
Input/output relation of such systems does not involve integrals or derivatives for CT systems and delay or shifts for DT systems.
Example:
y(t) = 5x(t)
y[n] = 15x2[n] + 10x[n]

## Slide 140
When the output of the system depends upon the present input sample and previous input and output, then system is called Dynamic system
Hence system need memory to store the previous input / output.
Equation Characterizing a dynamic system will always be a differential equation or difference equation.
Example:

## Slide 147
Time-Invariant and Time-Variant Systems (Shift- Invariant and Shift-Variant Systems)
The input - output characteristics of the system do not change with shift of time origin, such systems are called shift-invariant or time-invariant systems
Example:
Then system is said to be time-invariant if
It is very difficult to implement shift variant systems

## Slide 150
Determine whether the following system are shift invariant or not
      ]
Let the input be then
i.e. Replace n inside ] by
--------(1)
Let us delay output y [n] by k samples
----------------(2)
Hence the system is shift invariant / time invariant

## Slide 151
Note: ]
Let the input be then i.e. Replace n inside ] by
---------------(1)
Let us delay output y [n] by k samples
replace
----------------(2)
Hence the system is shift variant / time variant

## Slide 152
3.
Note:
So,
Let the input be x [n – k] then i.e. Replace n inside x[n] by (n – k)
---------------(1)
Let us delay output y [n] by k samples
replace
-------------(2)
Hence the system is shift variant / time variant

## Slide 153
Note:
So,
Let the input be then i.e. Replace n inside x[n] by n-k
Let the input be x (n – k) then
---------------(1)
Let us delay output y [n] by k samples
replace
-------------(2)
Hence the system is shift variant/ time variant

## Slide 158
Linear and Nonlinear Systems

## Slide 159
Linear or non linear?

## Slide 160
Linear or Non linear systems ?

## Slide 175
Casual and Non-Causal Systems
In Causal system the output depends upon only on past and present inputs but not on future inputs.
Example:
In Non-causal system the output depends upon future inputs also..
Example: ]
In real time, Non-causal systems are physically unrealizable. They are found in Image Processing, when the independent variable is not time !

## Slide 176
Determine whether the following System Are Causal Or Non-causal
      Ans : Causal
      Ans : Non-causal
      Ans: Non-Causal

## Slide 181
Stable and Unstable Systems
When every ‘bounded’ input produces a ‘bounded’ output, then the system is called Bounded-Input Bounded-Output (BIBO) Stable.
(finite number)
Then
(finite number)
If bounded input produces unbounded output then the system is unstable. The unstable system produces erratic (unpredictable behavior) output