## Slide 1: Engineering Materials

## Slide 2: Mechanical properties of Engineering Materials
Stiffness
Elasticity
Plasticity
Ductility
Brittleness
Malleability
Toughness
Hardness

## Slide 3
Stiffness: it is the ability of materials to resist deformation under the action of loads
Elasticity : Elasticity it is a property by which a material changes its shape when load is applied and will regain its original shape when load is removed.
Plasticity : it is the property by which a material is not able to regain its original shape when the load is removed.
Ductility : it is a property by which materials can be drawn into wires.
Malleability: it is a property by which materials are able to be beaten or converted into thin sheets.

## Slide 4
Brittleness : it is the ability of a material by which it can break or develop cracks when loaded.
Toughness: it is the property by which the material is able to resist shocks or impact loading.
Hardness : it is a property of a material by which it can resists scratches, wear and tear.
Creep: it is the ability of a materials undergo permanent deformation at constant stress (load) for long period of time.
Fatigue: it is the property of a material to resist repeatable and fluctuating loads.
Corrosion resistance: metals and alloys which can withstand the corrosion action of medium.

## Slide 5
Wear resistance: the ability of a material to resist friction wear under particular condition.
Tensile strength : this enables the material to resist the application of tensile force.
Shear strength: it is the ability of a material to resist shear force applied on material.
Compression strength : it is the ability of a material to withstand pressures acting on a given place.

## Slide 6
Stress : it is defined as internal reaction set up in the solid per unit cross sectional area.
Strain :it is the deformation expresses on the basis of unit dimension.

## Slide 7: Mechanical testing by engineering Materials
Hooks Law : it states that stress and strain are directly proportional to each other under elastic limit.
Notes: Experimental study by hooks revealed that the the elastic body regain its original shape when it is in elastic limit.

## Slide 8: Stress strain diagram
Notes: Stress : force per unit area that result from an applied load
Strain: physical deformation response of a material.
Stress strain diagram is a graph that represents how a part behaves under an increasing load.
S-S diagram undergoes 3 deformations
Elastic
Plastic
3. Rupture

## Slide 9
Modulus of resilience : is the work done on a unit volume of material as the force is gradually increased from O to P Nm/m3 .
Modulus of Toughness : is the work done on a unit volume of material as the force is gradually increased from O to R Nm/m3
Working stress : Actual stress of material under a given loading.
Allowable stress : the maximum safe stress that a material can carry
FOS: the ratio of ultimate strength to allowable strength (Brittle material), ratio of Yield strength to allowable strength (Ductile Material)
Notes: The resilience of material is ability to absorb energy without creating permanent distortion
Ability to absorb energy without causing break
4) The allowable stress should limited to a value not exceeding propotional limit
Since propotional limit is difficult to determine accurately, the allowable stress is taken as either yield point or ultimate strength by a FOS
The relationship b/n gauge length and cross sectional area of tensile test specimen can be given by L guage = 5.65  A

## Slide 10: Hardness
Resistance to penetration
Testing for hardness can be divided into 3 categories
Indentation test
Scratch tests
Rebound test

## Slide 11: Indentation test
Produce a permanent impression on the surface of material.
The stress used to create the impression can be related to both the yield and ultimate strengths of material
Types – 1. Brinell hardness test
2. Vickers Hardness test
3. Rockwell Hardness test.
Notes: Penetration is mainly depends on the hardness of material
Bcz hardness is a function of force and the impression

## Slide 12: 1. Brinell Hardness
Larger ball size precludes the use of brinell hardness for small objects.
Bcz., of spherical shape of indenter ball, the BHN for the same material will not be same for different load if same size ball is used
Notes: Critical component the larger indentation may produe failure.
Tool- Hardended steel – spherical shape
Softer materials like – Al, Cu, mild steel , Low cardon steel
Pricinciple of this test is based on area of penetration.

## Slide 13: 2. Vickers Hardness test
Disadvantages:
Slow because careful penetration is required.
Error in measuring the diagonal length.
Advantage :
Result is independent of load
Notes: Tool – diamond
Shape- pyramid with square base and an angle of 136 deg b/n opposite faces
Applicable for – high carbon steel, tunston and silicon carbides
Tool will produce just mark on the material
L- diagonal length of material
P – 0,1 to 1 kg tp 120 kg

## Slide 14: 3. Rockwell test
Tool – diamond
Shape – conical shape
Applicable – all types except some hard material
Principle of this test based on depth of penetration.
Notes: Tool penetrate deeper RHN no. is less
Indentor is not able to penetrate RHN no. is more

## Slide 15
Scratch test : it involves scratching progressively on material. (MOH scale )
Rebound test : employ techniques to assess the resilience of material by measuring changes in potential energy.
BHARCOL test : it is used for hard polymers and thermosetting polymers
KNOOP test : its used for micro size materials like sim cards and memory cards.
Notes: Hardness is measured reboundnace of material after removing thr indentor tool . More reboundness material is softer , less material is harder . Used for soft polymer, thermo plastic polymer.

## Slide 16: Ferrous Material
Main alloying element is Carbon
Based on amount of Carbon present, alloys will have different properties
Carbon content less than 1.5% called as Steel
Carbon Content between 2-4% called as Cast Iron
Classification of ferrous materials based on carbon content
Steels
Mild Steel (Low carbon Steel)
% of Carbon in Iron 0.15% to 0.25%
Moderately Strong and have a good weldability
Cost is also low
Medium Carbon Steel
% of Carbon in Iron 0.3% to 0.6%
High Strength and less weldability

## Slide 17
High Carbon Steels
% of Carbon in Iron 0.65% to 1.5%
More Harder and tough by heat treatment
Poor weldability
Cast Iron
Carbon Content between 2-4%
Cost of production is low
Grey Cast Iron
They are in the form of Graphite flakes
Weak and brittle
Possess good damping and resistance to wear
Application base structure, bed for heavy machines
White Cast Iron
Because of cementite fractured surface appears like white
They are very brittle and difficulty to machine
Application rollers in rolling mills (due to limited wear resistance property)

## Slide 18
Nodular (Ductile) Cast Iron
Small addition of Mg/Cr to grey CI melt before casting can result in graphite to form nodular or sphere like particle
They strong and ductile than grey CI
Applications- Pump bodies, Crank shaft, Automobile Components.. Etc
Malleable Cast Iron
There are formed after heat treatment of white CI (up to 800-900◦C
Strong and appreciable amount of ductility
Applications- Railroad, connecting rod, marine and other heavy duty vehicles

## Slide 19: Non Ferrous Materials
Substance composed of metals other than Iron
Some of ferrous materials are as follows
Alluminium Alloys
They are high thermal and electrical conductivities
Good corrosion resistance properties
FCC structure and ductile even at low temperature
Strength of these alloys can be increase by cold and heat treatment
They designated in two groups – cast and wrought
Main alloying elements includes – Cu, Si, Mn, Mg, Zn, Li and Ti
Applications- Beverage cans, automobile and aerospace parts

## Slide 20
Copper Alloys
Cu is softer and more ductile and hard to machine
Corrosive resistance property
These are strengthened by either cold work or solid soluble method
Common copper alloys – Brass (Cu and Zn) and Bronze (Cu and Sn)
Bronze are more stronger and corrosive resistance than brass
Good electrical conductivity and wear resistance
Applications – Costume jewellery, coins, musical instruments, electronics, springs, bushes, surgical and dental instruments, radiators..etc

## Slide 21
Magnesium Alloys
Low density among all structural metals
It has HCP structure
These are fabricated by casting or hot working
Major additional alloys are Al, Zn, and Mn
Applications- Saws, tools, automobile parts (Steering wheels, seat frame), electronics ( casing of laptops, cell phones)
Titanium Alloys
They are of relatively low density, high strength and high melting point
Easy to machine and forge
More expensive
Excellent corrosive resistance and wear resistance propeties
Applications- Space vehicles, Airplane structure , petroleum and chemical inductries.

## Slide 22: Plastics
Common organic materials are plastic and synthetic rubbers termed as organic polymers.
They have low specific gravity and good strength
Two important classes of organic polymers
Thermoplastics
On heating , these material become soft and hardened again upon cooling
E.g Nylon, polythene etc
Design requirement: strength
Applications: Valves, gears, cams, pistons, fan blades, …
Plastics: nylon, acetal (delrin), polycarbonate, phenolic
Design requirement: wear resistance
Applications: bearings, gears, bushings, wheels, ….
Plastics: nylon, acetal (delrin), polyurethane, phenolic, polymide
Thermosetting Plastics

## Slide 23
Thermosetting Plastics
Thermosetting plastics are cured into permanent shape. Cannot be re-melted to the flowable state that existed before curing, continued heating for a long time leads to degradation or decomposition. This curing (cross-linked) reaction is irreversible. Thermosets generally have better mechanical, thermal and chemical properties. They also have better electrical resistance and dimensional stability than do thermoplastics
Epoxies
Properties: good dimensional stability, excellent mechanical and electrical properties, good resistance to heat and chemicals
Applications: electrical components requiring strength, tools and dies, fiber reinforced epoxies are used in structural components, tanks, pressure vessels, rocket motor casing
Phenolics
Properties: good dimensional stability, rigid, high resistance to heat, water, electricity, and chemicals
Applications: laminated panels, handles, knobs, electrical components; connectors, insulators
Polyesters
Properties: good mechanical, electrical, and chemical properties, good resistance to heat and chemicals
Applications: boats, luggage, swimming pools, automotive bodies, chairs

## Slide 24
Abrasive Materials
Hard, Non metalic, Sharp edge and irregular shaped material
Used to remove small amount of materials by cutting action
Application in grinding, polishing, super finish etc
Materials are alumina, silicon carbide, cubic boron nitride and diamond
Ceramics
Compounds of metallic and non metalic materials
High compressive strength, low thermal expansion, high elasticity, high hardness, high wear resistance and low electrical and thermal conductivity
Used for tiles, pottery wares etc
Silica
Available in the form of quartz
Most of the glasses contain more than 50% of silica
Used in electrical materials to increase magnetic permeability of the material
Glass
It is Amorphous material, It consist more than 50% silica
Used in windows, container, lightining, cookware etc